## Slide 1: LECTURER 2
  Engineering and True Stress-Strain
  Diagrams
  Ductile materials
  Brittle material

## Slide 2: Engineering and True Stress-Strain Diagrams
In order to study the plastic flow of materials, it is necessary to understand the concepts of true stress and true strain.
In tensile test, during the test progresses, one region of the specimen begins to deform much quicker than the rest.
In order to calculate the stress there are two possibilities – the original area or the actual area of the specimen at any instant of the load.
When the stress is calculated on the basis of the original area, it is called the engineering or nominal stress.
If the original length is used to calculate the strain, then it is called the engineering strain.

## Slide 3: Engineering and True Stress-Strain Diagrams
The nominal stress σn = P/A0
where P is the force and A0 the original area of cross section
The nominal strain, εn = (L-L0)/L0
where L is the length of the original gauge length under force P, and L0 is the original gauge length.

## Slide 4: Engineering and True Stress-Strain Diagrams
The stress is calculated based on the instaneous area at any instant of load, then it is the true stress.
Where,
Ai is the actual area of the cross-section corresponding to load P.

## Slide 5: Engineering and True Stress-Strain Diagrams
Normal Strain (ε) is given as
Since

## Slide 6: Engineering and True Stress-Strain Diagrams
Similarly, True strain
Where,
dℓ is the infinitesimal elongation, ℓi is the instaneous length and ℓ0 is the original length.
In we assume that the volume change during plastic deformation can be neglected and
using Eq (1) 

## Slide 7: Engineering and True Stress-Strain Diagrams
Fr copper the rapid area reduction that accompanies necking causes the curve to fall. This does not happen with true stress-true strain curve.
The strain is not homogenous after necking begins, when one part of the specimen is elongating more than the rest, then it is meaningful to use the entire specimen length for finding deformation.

## Slide 8: Engineering and True Stress-Strain Diagrams
Both engineering and true stress and strain diagrams are having large scale of application in engineering practice.
Engineering stress and strain diagrams are usually used in the elastic range, while true stress – strain diagrams are used in plastic range.
Most of the diagram used for practical purposes are based on engineering stress versus engineering strain, while true stress – true strain diagrams are required occasionally.

## Slide 9: Ductile materials
A body is said to have yielded or to have undergone plastic deformation if it does not regains its original shape when a load is removed.
The resulting deformation is called permanent set. If permanent set is obtainable, the material is said to exhibit ductility.
Ductility measures the degree of plastic deformation sustained it fracture.
One way of specify a material is by the percentage of elongation (%EL).
Percentage of elongation =

## Slide 10: Ductile materials
A ductile material is one with a large Percentage of elongation before failure.
The magnitude of percentage of elongation will depend on the specimen length.
Material | Percentage of Elongation
Low-Carbon | 37%
Medium-Carbon | 30%
High-Carbon | 25%

## Slide 11: Ductile materials
For ductile material, the ultimate tensile and compressive strength have approximately the same absolute value.
The steel is ductile material because it far exceeds the 5% elongation.
High strength alloys, such as spring steel, can have 2% of elongation but even this is enough to ensure that the material yields before it fractures.
Hence it is behaved like a ductile material. Gold is relatively ductile at room temperature. Most of the material becomes ductile by increasing the temperature.

## Slide 12: Ductile materials
Properties of ductile materials:
Easily drawn into wire or hammered thin.
Easily molded or shaped.
Capable of being readily persuaded or influenced tractable.
Easily stretched without breaking in material strength.

## Slide 13: Stress – strain behavior of ductile materials
In the case of ductile materials at the beginning of the tensile test, the material extends elastically.
The strain at first increase proportionally to the stress and the specimen returns to its original length on removal of the stress.
The limit of proportionality is the stage up to which the material obeys Hooke’s law perfectly.
Beyond the elastic limit the applied stress produces plastic deformation so that a permanent extension remains even after the removal of the applied load.
In this stage the resultant strain begins to increase more quickly than the corresponding stress and continues to increase till the yield point is reached. At the yield point the material suddenly stretches.

## Slide 14: Stress – strain behavior of ductile materials
The rate of applied load to original cross-sectional area is termed the nominal stress.
This continues to increase with elongation, due to strain hardening or work hardening, until the tensile stress is maximum.
This is the value of stress at maximum load and can be calculated by dividing the maximum load by the original cross-sectional area. This stress is called ultimate tensile stress.

## Slide 15: Stress – strain behavior of ductile materials

## Slide 16: Stress – strain behavior of ductile materials
stress-strain diagram for ductile material (mild steel) showing the limit of proportionality, elastic limit, yield point, ultimate tensile stress and fracture.
At a certain value of load the strain continues at slow rate without any further stress. This phenomenon of slow extension increasing with time, at constant stress is termed creep.
At this point a neck begins to develop along the length of the specimen and further plastic deformation is localized within the neck.
After necking the nominal stress decreases until the material fractures at the point of minimum cross-sectional area.

## Slide 17: Brittle material
Brittle material is one which is having very low percentage of elongation.
Brittle materials break suddenly under stress at a point just beyond its elastic limit.
A Brittle material exhibits little or no yielding before failure.
Brittle material will have a much lower elongation and area reduction than ductile ones. The tensile strength of Brittle material is usually much less than the compressive strength.
The brittle material can be deformed in a ductile only under the conditions of high pressure.
Grey cast iron is a best example for brittle material

## Slide 18: Determination of Brittle materials
If the percentage of elongation is at or below 5%, assume brittle behavior.
If the ultimate compressive strength is greater than the ultimate tensile strength assume brittle behavior
If no yield strength is occurred suspect brittle behavior

## Slide 19: Stress – strain behavior of brittle materials
For the determination of yield strength in such materials, one has to draw a straight line parallel to the elastic portion of the stress strain curve at a predetermined strain ordinate value (say 0.1%).
The point at which this line intersects the stress-strain curve is called the yield strength.